## Slide 1
ECE408/CS483/CSE408 Fall 2017
Convolutional Neural Networks
Carl Pearson
pearson@Illinois.edu

## Slide 2
Deep Learning in Computer Vision
Chart: Accuracy

## Slide 3
Consider a 250 x 250 image
  Vectorize the 2D image to a 1D vector as input feature
  Each hidden node would requires 250x250 weights ~ 62,500
  How about multiple hidden layer? Bigger image?
  Too many weights, computational and memory expensive
Traditional feature detection in image processing
  Filters  Convolution kernels
  Can we use it in neural networks?
MLP for an Image

## Slide 4
2-D Convolution
1
2
3
2
1
2
3
4
3
2
3
4
5
4
3
2
3
4
3
2
1
2
3
2
1
1
4
9
8
5
4
9
16
15
12
9
16
25
24
21
8
15
24
21
16
5
12
21
16
5
W
X
Y
1
2
3
4
5
6
7
2
3
4
5
6
7
8
3
4
5
6
7
8
9
4
5
6
7
8
5
6
5
6
7
8
5
6
7
6
7
8
9
0
1
2
7
8
9
0
1
2
3
1
2
3
4
5
2
3
4
5
6
3
4
321
6
7
4
5
6
7
8
5
6
7
8
5

## Slide 5
Convolution vs Fully-Connected
+
b
W0
W5
W1
w0,0
w1,0
w0,1
+
…
…
…
x0
x5
x1
…
…
…
x0,0
x1,0
x0,1
…
…
…

## Slide 6
Applicability of Convolution
Fixed-size inputs
Variably-sized inputs
  Varying observations of the same kind of thing
    Audio recording of different lengths
    Image with more/fewer pixels

## Slide 7
Example Convolution Inputs
 | Single-channel | Multi-channel
1-D | Audio waveform | Skeleton animation data: 1-D joint angles for each join
2-D | Fourier-transformed audio data Convolve frequency axis: invariant to frequency shifts Convolve time axis: invariant to shifts in time | Color image data: 2-D data for R,G,B channels
3-D | Volumetric data, e.g. medical imaging | Color video: 2-D data across 1-D time for R,G,B channels
Deeplearningbook.org, ch 9, p 355

## Slide 8
LeNet-5:CNN for hand-written digit recognition

## Slide 9
Anatomy of a Convolution Layer
Input features/channels
A inputs (N1 × N2)
Convolution Layer
B convolution kernels (K1 × K2)
Output Features/channels
A × B outputs (N1 – K1/2) × (N2 – K2/2)

## Slide 10
A subsampling layer
  Sometimes with bias and non-linearity built in
Common types: max, average, L2 norm, weighted average
Helps make representation invariant to small translations in the input
Aside: 2-D Pooling

## Slide 11
Sparse interactions
  Meaningful features in small spatial regions
  Need fewer parameters (less storage, better statistical characteristics, faster training)
  Need multiple layers for wide receptive field
Why Convolution (1)

## Slide 12
Parameter sharing
  Kernel is reused when computing layer output
Equivariant Representations
  If input is translated, output is translated the same way
  Map of where features appear in input
Why Convolution (2)
w0,0
w1,0
w0,1
+
…
x0,0
x1,0
x0,1
+
…
y0,0
y1,0
y0,1

## Slide 13
Convolution
2-D Matrix
Y = W ⊗ X
Kernel smaller than input: smaller receptive field
Fewer Weights
MLP
Vector
Y = w x + b
Maximum receptive field
More weights

## Slide 14
Forward Propagation

## Slide 15
Example of the Forward Path of a Convolution Layer

## Slide 16
void convLayer_forward(int B, int M, int C, int H, int W, int K, float* X, float* W, float* Y) {
int H_out = H – K + 1;
int W_out = W – K + 1;
for (int b = 0; b < B; ++b) // for each image in batch
for(int m = 0; m < M; m++) // for each output feature map
for(int h = 0; h < H_out; h++) // for each output element
for(int w = 0; w < W_out; w++) {
Y[m, h, w] = 0;
for(int c = 0; c < C; c++) // sum over all input feature maps
for(int p = 0; p < K; p++) // KxK filter
for(int q = 0; q < K; q++)
Y[b, m, h, w] += X[b, c, h + p, w + q] * W[m, c, p, q];
}
}
Sequential Code: Forward Convolutional Layer

## Slide 17
void poolingLayer_forward(int B, int M, int H, int W, int K, float* Y, float* S) {
for (int b = 0; b < B; ++b) // for each image in batch
for (int m = 0; m < M; ++m) // for each output feature maps
for (int h = 0; x < H/K; ++h) // for each output element
for (int w = 0; y < W/K; ++y) {
S[m, x, y] = 0.;
for (int p = 0; p < K; ++p) // loop over KxK input samples
for (int q = 0; q < K; ++q)
S[b, m, h, w] += Y[b, m, K*x + p, K*y + q] /(K*K);
}
S[b, m, h, w] = sigmoid(S[b, m, h, w] + b[m]) // bias, non-linearity
}
Sequential Code: Forward Pooling Layer

## Slide 18
void unroll(int B, int C, int H, int W, int K, float* X, float* X_unroll) {
int H_out = H – K + 1;
int W_out = W – K + 1;
for (int b = 0; b < B; ++b)
for (int c = 0; c < C; ++c) {
int w_base = c * (K*K);
for (int p = 0; p < K; ++p)
for (int q = 0; q < K; ++q) {
for (int h = 0; h < H_out; ++h)
for (int w = 0; w < W_out; ++w) {
int w_unroll = w_base + p * K + q;
int h_unroll = h * W_out + w;
X_unroll[b, h_unroll, w_unroll] = X[b, c, h + p, w + q];
}
}
}
Function to generate “unrolled” X

## Slide 19
Backpropagation

## Slide 20
void convLayer_backward_dgrad(int B, int M, int C, int H, int W, int K, float *dE_dY, float *W, float *dE_dX) {
int H_out = H – K + 1;
int W_out = W – K + 1;
for (int b = 0; b < B; ++b) {
for (int c = 0; c < C; ++c)
for (int h = 0; h < H; ++h)
for (int w = 0; w < W; ++w)
dE_dX[b, c, h, w] = 0;
for (int m = 0; m < M; ++m)
for (int h = 0; h < H_out; ++h)
for (int w = 0; w < W_out; ++w)
for (int c = 0; c < C; ++c)
for (int p = 0; p < K; p)
for (int q = 0; q < K; ++q)
dE_dX[b, c, h + p, w + q] += dE_dY[b, m, h, w] * W[m, c, p, q];
}
}
Calculating dE/dX

## Slide 21
Backpropagation

## Slide 22
void convLayer_backward_wgrad(int B, int M, int C, int H, int W, int K, float *dE_dY, float *X, float *dE_dW) {
const int H_out = H – K + 1;
const int W_out = W – K + 1;
for (int b = 0; b < B; ++b) {
for(int m = 0; m < M; ++m)
for(int c = 0; c < C; ++c)
for(int p = 0; p < K; ++p)
for(int q = 0; q < K; ++q)
dE_dW[b, m, c, p, q] = 0;
for(int m = 0; m < M; ++m)
for(int h = 0; h < H_out; ++h)
for(int w = 0; w < W_out; ++w)
for(int c = 0; c < C; ++c)
for(int p = 0; p < K; ++p)
for(int q = 0; q < K; ++q)
dE_dW[b, m, c, p, q] += X[b, c, h + p, w + q] * dE_dY[b, m, c, h, w];
}
}
Calculating dE/dW